## Slide 1: GEOCHEMICAL AND PETROPHYSICAL TRANSFORMATIONS DURING ROCK-FLUID INTERACTIONS IN CANEY FORMATION, SOUTH CENTRAL OKLAHOMA
Presenter: Gabriel Adua Awejori
57th South Central Geological Society of America Conference 2023, Stillwater, Oklahoma
Awejori, G.A., Radonjic, M.
Oklahoma State University, Stillwater, Oklahoma, USA
Doughty, C., Dong, W.
Energy Geosciences Division, Lawrence Berkeley National Laboratory, Berkeley, California, USA
Paronish, T.
Leidos Research Support Team, National Energy Technology Laboratory, Morgantown, West Virginia, USA
DOE Award DE-FE0031776 from the Office of Fossil Energy in Partnership with Continental Resources, OGS, OSU Geology, OSU Chem. Engineering, University of Pittsburgh, Lawrence Berkeley National Lab and DOE NETL.

## Slide 2: PRESENTATION OUTLINE
Introduction
Objectives
Materials and Methodology
Results and Discussions
Conclusions
Fig. 1: Caney core on display at workshop in OKC, February 2020

## Slide 3: INTRODUCTION
The Caney Formation is of Upper Mississippian age and correlates with Barnett Shale of Northern Texas and the Fayetteville Shale of Northeastern Oklahoma
Area for our work is the Caney Formation in the Ardmore Basin
This formation is replete with hydrocarbons but has high clay content that renders it an ultra low permeability formation
However, advancements in horizontal drilling and fracturing technologies makes it profitable to recover hydrocarbons from this formation
Knowledge on geochemical responses of the formation to Hydraulic Fracturing Fluids (HFFs) is currently limited
Fig. 2: Geological map of Oklahoma, showing Ardmore Basin area and location of Caney Wells (Blue Star)
Location of Caney Well

## Slide 4: OBJECTIVES
Our work is aimed at achieving the following objectives:
To undertake comprehensive evaluation of chemical and mineralogical composition of Caney Formation
To explore the geochemical response of the formation to Hydraulic Fracturing Fluid (HFF) – Mineralogical Changes and scale formation
To assess the potential of clay swelling, migration of fines
To evaluate the impact of mineralogical changes, scale formation and clay minerals on petrophysics of the reservoir
Fig. 3: Schematic of Geochemical Rock-Fluid Interaction following hydraulic fracturing of reservoir formation
Scale formation
Clay fines migration
Mineral Precipitation
Wellhead
Hydraulic Fractures
Fracking Fluid
Clay fines migration
Mineral Dissolution
Hydraulic Fractures

## Slide 5: MATERIALS AND METHODOLOGY
Rock
Powder
Fluid
Oven
Well V
V1
V2
V3
Fracturing Fluid
95oC
Atm. Pressure
Well H
H1
H1
H1
Deionized
Water
7-days
30-days
X-Ray Diffraction
Scanning Electron Microscopy
Inductively Coupled Plasma Mass Spectroscopy
Energy Dispersive Spectroscopy
Before
After
Mineralogical Compositions
Chemical Compositions
Effluent Chemistry
Microstructure
Characterization of Alterations caused by Geochemical Reaction
STATIC BATCH EXPERIMENT
DATA ACQUISITION
DATA ANALYSES AND INTEGRATION

## Slide 6: RESULTS
Initial Mineralogical Compositions of Rock Samples
Predominant minerals in rocks are Quartz, Feldspar, Carbonate and Illite with subordinate Pyrite
Two samples were taken for two sampling intervals in Well V. These were sampled at close interval (˜5ft)
Significant difference in mineralogy of samples taken from the same sampling interval highlights the highly heterogeneous nature of formation

## Slide 7: RESULTS
Mineralogical Composition Changes of Rock Samples – Well V
Mineralogical changes observed in Well V samples are as follows:
Pyrite breakdown occurs mostly within the first 7 days of reaction
Composition of quartz drops after 7 days but remains relatively constant after that
Feldspar composition generally shows a downward trend after reaction for 7 days and 30 days respectively
Illite composition shows an increasing trend over 7 days and 30 days

## Slide 8: RESULTS
Mineralogical changes observed in Well H samples are as follows:
Pyrite breakdown occurs mostly within the first 7 days of reaction
Composition of quartz drops after 7 days but remains relatively constant after that
Feldspar composition generally shows a downward trend after reaction for 7 days and 30days respectively
Illite composition shows an increasing trend over 7 days and 30 days
Mineralogical Composition Changes of Rock Samples – Well H

## Slide 9: RESULTS – Post-Reaction XRD Peaks
Background compositions increased rapidly in the first 7-days and largely within the clay portions of the XRD peaks – Amorphous phases
Amorphous phases in the clay section may be due to dispersion of clays during rock-fluid interactions
Qtz
Clay
Carbonates
Clay
Qtz
Carbonates
Graph: XRD Peaks for Reacted and Unreacted Samples from Well H
Results from XRD analyses of samples after reacting for 7-days and 30-days respectively showed reduction in peaks of most samples (quartz, feldspars and carbonates)
Peak reduction due to mineral dissolution

## Slide 10: RESULTS
Fluid composition is the main driving force for dissolution and precipitation kinetics
Though dissolution of calcium is observed, it is not as dramatic as observed in our previous work (acidized fluid)
Calcium concentrations in effluent is relatively stable because, fracturing fluid used for experiment had an approximately neutral pH
Dissolution of pyrite causes temporal acidity which lead to dissolution of carbonates thus the marginal increases in Ca concentrations
Cation exchange in clay sites also causes subtle fluctuations in Ca concentration in effluent
Chart: Ca Concentration
0 days | 64587.6678 | 64587.6678 | 64587.6678 | 64587.6678 | 64587.6678
7 days | 64553.7075 | 79761.0079 | 76438.0926 | 64662.1624 | 67431.3124
30 days | 74269.4737 | 68096.3221 | 76177.1033 | 77720.5657 | 69471.5693

## Slide 11: RESULTS
The high concentrations of Si observed on the graphs cannot be explained by quartz dissolution at the given condition
Dissolution of feldspar contributes to Si concentration in effluent
The Si concentration in effluent can be the result of the dissolution of biogenic silica which is common in the Caney formation.
Chart: Si Concentration
0 days | 6011.3891 | 6011.3891 | 6011.3891 | 6011.3891 | 6011.3891
7 days | 15838.8159 | 15244.6249 | 17204.3504 | 34429.4148 | 18478.708
30 days | 58376.2917 | 30831.6628 | 27068.3162 | 30624.8211 | 46484.4912

## Slide 12: RESULTS
Aluminum in effluent is mainly from the dissolution of feldspars
Aluminum entering solution is precipitated at a fast rate
The formation of clays and Al-based minerals through precipitation is thus responsible for loss of Al in effluents
Aluminum decrease could also be caused by ion exchange at clay sites
Al remains relatively low and after initial release Al drops in elemental concentrations
Chart: Al Concentration
| V2 | V3 | H1 | H2 | H3
0 days | 272.6525 | 272.6525 | 272.6525 | 272.6525 | 272.6525
7 days | 359.2236 | 415.836 | 326.738 | 307.6723 | 309.5257
30 days | 293.9724 | 265.236 | 300.7823 | 300.9494 | 298.3326

## Slide 13
Cl: clays
Dol: Dolomite
Cal: Calcite
Py: Pyrite
OM: organic matter
OM
Dol
Cal
SEM
Py
Cl
Cal
Dol
Cal
Microstructure of sample shows heterogeneity of the formation
Dissolution of pyrites creates a localized pH drop
Carbonates dissolve in response to pH drop, creating voids that increase permeability
Feldspars breakdown to form more clay minerals in the formation
Dissolution of minerals cause increased ionic composition of fluids
High ionic compositions lead to precipitation of new minerals
EDS
RESULTS

## Slide 14: CONCLUSIONS
Oxygenated fluids cause breakdown of pyrite, which introduces acidity in fluid to cause breakdown of carbonates
Increased Ca concentration due to breakdown of Carbonates
High Si concentration in effluent from breakdown of feldspar, biogenic silica and exchange at clay mineral sites
The uptake of Al and Mg elements is believed to be in precipitation of clay minerals (illite)
During reaction, feldspar composition decreases whilst illite composition increases
Break down of feldspar and formation of clay minerals leads to introduction of ductile behavior in rock
Confining pressures are effective in closing fractures under ductile conditions

## Slide 15: ACKNOWLEDGEMENTS
The authors acknowledge:
DOE Award DE-FE0031776 from the Office of Fossil Energy’s, Oil and Natural Gas Program, U.S. Department of Energy
Joseph Renk, Technical Project Officer, National Energy Technology Laboratory
Lisa Whitworth and Brent Johnson of Oklahoma State University Microscopy Laboratory
Brian Killian and Barry Dean of Continental Resources for providing samples and Caney well production histories respectively
The authors are grateful to Barrier Material and Geomimicry laboratory and Research Group; Dr. Xiong Fengyang and Dr. Allan Katende for their support

## Slide 16: REFERENCES
Dove, P.M. 1995. Kinetic and thermodynamic controls on silica reactivity in weathering environments, in: White, A.F. and Brantley, S.L. (eds). Chemical Weathering Rates of Silicate Minerals. pp. 235–290.
Knauss, K.G., and T.J. Wolery. 1988. The dissolution kinetics of quartz as a function of pH and time at 70 C. Geochim. Cosmochim. Acta 52, 43–53.
Olabode, A.O. 2017. Diagenesis and Formation Stress in Fracture Conductivity of Shaly Rocks; Experimental-Modelling Approach in CO2-Rock Interactions.
Tester, J.W., W.G. Worley, B.A. Robinson, C.O. Grigsby, and J.L. Feerer. 1994. Correlating quartz dissolution kinetics in pure water from 25 to 625C. Geochim. Cosmochim. Acta 58, 2407–2420.

## Slide 17: THANK YOU