## Slide 1: Post-Fracturing Rock-Fluid Reactions in Sub-Surface Caney Shale of Southern Oklahoma
Presenter: Gabriel Awejori
DOE Award DE-FE0031776 from the Office of Fossil Energy in Partnership with industry partner, OGS, OSU Geology, OSU Chem. Engineering, University of Pittsburgh, Lawrence Berkeley National Lab and DOE NETL.

## Slide 2: PRESENTATION OUTLINE
Overview
Problem
Objectives
Materials and Methodology
Results and Discussions
Conclusions
Plans Going Forward

## Slide 3
Contributions from conventional and unconventional sources to total hydrocarbon production in USA
OVERVIEW – Conventional versus Unconventional
Source: US Energy Information Administration

## Slide 4
OVERVIEW - PROJECTIONS
Contribution of unconventional hydrocarbon sources to total production is projected to increase
Graphs below show contributions for various scenarios
High Technology Development
Low Technology Development
High Petroleum Prices
Low Petroleum Prices
Source: US Energy Information Administration

## Slide 5
Contributions from various unconventional sources to total unconventional production in USA
Caney Shale is categorized under Mississippian Shales in Oklahoma
Source: US Energy Information Administration
OVERVIEW – Caney Shale Contribution

## Slide 6
PROBLEM
Recent statistics of unconventional shale reserves in the USA are estimated at approximately, 6 trillion barrels of oil and 495 trillion cubic feet of gas (Farrokhrouz et al., 2022)
Complex mineralogy and ultra-low permeability of shale reservoir makes development and production of these reservoirs challenging (Swami et al., 2012)
Current recovery from shale reservoirs is just about 10% of original hydrocarbons in place (Mukhina et al., 2021)
Current research aims to understand these reservoirs to help create technologies that will enhance recovery
Locations of unconventional hydrocarbon deposits in the United States of America (https://www.ireservoir.com/case_shale.html, accessed on May 12, 2023)

## Slide 7: PROBLEM – Specific Area
The Caney Shale is located in the Ardmore Basin of South-Central Oklahoma Oil Province (SCOOP)
It overlies the better-known Woodford Shale which has been the main target of drilling in the area over the years
The Caney Shale, though replete with hydrocarbons, is characterized by high clay content, complex mineralogy, and ultra-low permeability
This makes hydraulic fracturing the most viable option in producing from this shale
This study characterizes the long-term geochemical responses of the Caney Shale after hydraulic fracturing
Geological map of Oklahoma, showing SCOOP area (red ellipsoid) and well locations (red star) (after Johnson, 2008)

## Slide 8: OBJECTIVES
This work is designed to investigate the impact of geochemical rock-fluid reactions on permeability of Caney Shale
The following sub-objectives culminate in achieving this objective:
Evaluating the mineralogy of Caney Shale in South Central Oklahoma Province (SCOOP)
Understanding the microstructural configuration and spatial heterogeneity of the Caney Shale
To evaluate potential geochemical rock-fluid interactions in Caney Shale
To identify the mechanisms controlling geochemical rock-fluid interaction in the Caney Shale and the factors that enhance or reduce these mechanisms
To assess the impact of rock-fluid interactions on evolution of petrophysical (permeability and porosity) and mechanical properties of Caney Shale
Fracture and near-fracture Rock-Fluid Interaction following hydraulic fracturing of reservoir formation

## Slide 9: MATERIALS AND METHODLOGY
Rock samples used for this experiment are recovered from two different wells as follows:
Well 1:
  Vertical well across entire Caney Shale
  Samples are recovered as cored-rock
Well 2:
  Horizontal well drilled within Reservoir 3
  Samples are recovered as rock-cuttings at 1000ft intervals
Rock samples are prepared and ground into powders with average particle size of 30µm
Field Fracturing Fluid and Field Produced Brines recovered from Caney Shale were the main reacting fluids. Deionized water was used as a standard for comparison
Relative positions of two wells and sample locations: Samples V1 to V5 are cored-rocks from five (5) zones of the formation. H1 to H3 are rock cuttings spaced 1000ft horizontally at approximately the same vertical depth (Schematic not drawn to scale)
V1
V2
V3
V4
V5
H1
H2
H3
Well 1
Well 2
Reservoir 1
Ductile 1
Reservoir 2
Reservoir 3
Ductile 2

## Slide 10
MATERIALS AND METHODLOGY
Rock Powder
Fluids
Oven
X-ray Diffraction (XRD)
Scanning Electron Microscopy (SEM)
Inductively Coupled Plasma Mass Spectroscopy (ICPMS)
Energy Dispersive Spectroscopy (EDS)
Before
After
Mineralogical Compositions
Chemical Compositions
Effluent Chemistry
Microstructure
Characterization of Alterations caused by Geochemical Reaction
SAMPLE PREPARATION AND STATIC BATCH REACTOR EXPERIMENT
LABORATORY TECHNIQUES AND DATA ACQUISITION
DATA ANALYSES, INTEGRATION AND INTERPRETATION
Vertical Well (Cored-Rock)
Horizontal Well (Rock-Cuttings)
Exp 1: Synthetic Fracturing Fluids
Exp 2: Field Fracturing Fluid
Exp 3: Field Produced Fluid
Standard: Deionized Water
Conditions: 95oC (203oF), 14.7psi
(200mL:1g) Avg ps =30µm
Exp 2 & 3: 7 and 30 days
(150mL:1g) Avg ps =30µm
Flow chart of materials and methodology used in preliminary experiments, data acquisition and interpretation

## Slide 11
RESULTS – Mineralogical Alterations of Caney Shale Powders in Field Fracturing Fluids (HF)-XRD analysis
Pyrite breakdown occurs mostly within the first 7 days of reaction
The amount of quartz drops after 7 days but remains relatively constant after that.
Feldspar presence generally shows a downward trend after reaction at both 7 and 30 days
The amount of illite is increasing continuously at 7 and 30 days.
V – Vertical Well
(7) – 7days reaction
(30) – 30days reaction

## Slide 12
RESULTS – Mineralogical Alterations of Caney Shale Powders in Field Fracturing Fluids (HF)-XRD analysis
Pyrite breakdown occurs mostly within the first 7 days of reaction
The amount of quartz drops after 7 days but remains relatively constant after that.
Feldspar presence generally shows a downward trend after reaction at both 7 and 30 days
The amount of illite is increasing continuously at 7 and 30 days.
H – Horizontal Well
(7) – 7days reaction
(30) – 30days reaction

## Slide 13
RESULTS – Big Picture
Ternary diagram showing Comparison of unreacted samples to 7 days and 30 days reacted samples – Hydraulic Fracturing Fluids
The ternary diagram shows the changes in mineralogy that occurred due to geochemical rock fluid interactions
Mineralogy of rocks are originally closer to quartz, feldspar field which represents the brittle component of the formation
The breakdown of feldspar, pyrite and carbonates after 7days of reaction shifts the mineralogy towards phyllosilicates
After 30days of reaction, the mineralogy shifts moderately towards quartz-feldspar field but not enough to regain the original rigid and brittle characteristics
Shift towards phyllosilicates introduces a ductile character into the rocks

## Slide 14
Ca concentrations relatively stable because, fracturing fluid used for experiment had a circumneutral pH
Dissolution of pyrite causes transient acidity which initiates dissolution of carbonates
Cation exchange in clay sites also causes Ca concentration in effluent
High concentrations of Si observed on the graphs cannot be explained by quartz dissolution at the given conditions
Dissolution of feldspar contributes to Si concentration in effluent
Dissolution of biogenic silica could explain high Si concentrations
Al is mainly from the dissolution of feldspars
Al entering solution is precipitated at a fast rate – Clays and Al-based minerals
Similar trends observed for Mg and Fe
Chart: Ca Concentration
0 days | 64587.6678 | 64587.6678 | 64587.6678 | 64587.6678 | 64587.6678
7 days | 64553.7075 | 79761.0079 | 76438.0926 | 64662.1624 | 67431.3124
30 days | 74269.4737 | 68096.3221 | 76177.1033 | 77720.5657 | 69471.5693
Chart: Si Concentration
0 days | 6011.3891 | 6011.3891 | 6011.3891 | 6011.3891 | 6011.3891
7 days | 15838.8159 | 15244.6249 | 17204.3504 | 34429.4148 | 18478.708
30 days | 58376.2917 | 30831.6628 | 27068.3162 | 30624.8211 | 46484.4912
Chart: Al Concentration
| V2 | V3 | H1 | H2 | H3
0 days | 272.6525 | 272.6525 | 272.6525 | 272.6525 | 272.6525
7 days | 359.2236 | 415.836 | 326.738 | 307.6723 | 309.5257
30 days | 293.9724 | 265.236 | 300.7823 | 300.9494 | 298.3326
RESULTS - Elemental Composition of Caney-HF Fluid after Experiment (ICPMS)

## Slide 15
Modeling of experiment shows most elemental concentrations in effluent matching with ICP-MS results
Due to limitations in complete characterization of rock and fluids, some assumptions were made in the model
These assumptions and limitations of model are captured in the next slide
RESULTS – Model of Experiment (TOUGHREACT Simulator with Thermodderm Thermodynamic Database) by LBNL

## Slide 16: RESULTS – Model of Experiment
The following uncertainties and limitations are worth noting about modeling of experiment:
Thermodynamic data/models
  Modeled minerals of mixed composition (e.g. clays) may not have the same composition as in the rock formation
  Fluid salinity may exceed the validity range of the implemented ion activity model (extended Debye-Hückel)
Reconstruction of the Fracturing compositions
  Anion concentrations computed from assumptions Organic compounds besides acetate were neglected (unknown potential effects on experimental results)
Rock formation mineralogy
  Trace or amorphous minerals (undetected by XRD) impact the system geochemistry – amounts and types were assumed
Sampling effects
  Interactions with atmosphere (O2, CO2 impact pH and redox) Mineral reaction rates (kinetic constants, surface area)

## Slide 17
RESULTS - Mineralogical Alterations in Vertical Well Samples
Pyrite dissolution occurs within the first 7 days of reaction
Quartz reduces in the first 7 days but increases between 7 to 30 days whilst carbonate is relatively stable
Feldspar composition reduces and completely breakdown after 30 days
Illite composition shows an increasing trend over 7 days but remains relatively the same between 7 days and 30 days
V – Vertical Well
(7) – 7 days reaction
(30) – 30 days reaction

## Slide 18
RESULTS - Mineralogical Alterations in Horizontal Well Samples
Pyrite breakdown occurs within the first 7 days of reaction
Composition of quartz drops after 7 days but increases between 7 to 30 days
Feldspar reduces continuously and mostly dissolve or transform by 30 days
Illite composition shows an increasing trend after 7 days reaction and decreases between 7 and 30 days
H – Horizontal Well
(7) – 7 days reaction
(30) – 30 days reaction

## Slide 19
RESULTS – Big Picture
Comparison of unreacted samples to 7 days and 30 days reacted samples – Produced Fluids
The ternary diagram gives a big picture of impacts of mineralogical changes on rock properties
Mineralogy of rocks are originally closer to quartz and pyrite, indicating brittleness
Rock-fluid reaction shifts the samples to phyllosilicate zone, indicating ductility
Ductility promotes fracture healing thus loss of permeability
Main reactions that promote shift include:
  Breakdown of pyrite and microcrystalline quartz
  Breakdown of feldspar and carbonates
  Formation of illite

## Slide 20
RESULTS - Elemental Composition of Caney-Produced Fluids after Experiment (ICPMS)
Due to approximate neutral pH, Ca concentrations relatively stable
Dissolution of carbonates occur due to transient acidity caused by dissolution of pyrite
Precipitation or cation exchange in clay sites may lead to Ca uptake from effluent causing decreased Ca concentrations
The high Si concentrations cannot be explained only by the dissolution of quartz at the experiment conditions
Dissolved biogenic (microcrystalline quartz) or amorphous silica could explain high silica concentrations
Dissolution of feldspar contributes to Si concentration in effluent
Al is mainly from the dissolution of feldspars
Al concentrations are very low due to uptake from fluid – illite and other Al-based mineral precipitation
Similar trends observed for Magnesium (Mg) and Iron (Fe)
Chart: Ca Concentration
| V1 | V2 | V3 | V4 | V5 | H1 | H2 | H3
0 days | 494052.2577 | 494052.2577 | 494052.2577 | 494052.2577 | 494052.2577 | 494052.2577 | 494052.2577 | 494052.2577
7 days | 406614.8321 | 441292.5619 | 403210.5147 | 466723.9245 | 394016.0823 | 421729.7828 | 428776.6468 | 463751.3979
30 days | 431069.7043 | 412014.7063 | 410863.8242 | 439798.5718 | 474640.5789 | 438092.808 | 456574.8855 | 469422.0262
Chart: Si Concentration
| V1 | V2 | V3 | V4 | V5 | H1 | H2 | H3
0 days | 22182.6354 | 22182.6354 | 22182.6354 | 22182.6354 | 22182.6354 | 22182.6354 | 22182.6354 | 22182.6354
7 days | 26156.7483 | 39861.674 | 34208.9818 | 26551.1619 | 22421.1461 | 26178.5648 | 40650.5829 | 24740.6883
30 days | 55978.7873 | 56257.7372 | 61934.8532 | 49012.8589 | 42277.2656 | 49179.5693 | 49306.7985 | 51828.4391
Chart: Al Concentration
| V1 | V2 | V3 | V4 | V5 | H1 | H2 | H3
0 days | 107.7826 | 107.7826 | 107.7826 | 107.7826 | 107.7826 | 107.7826 | 107.7826 | 107.7826
7 days | 170.4136 | 343.7413 | 171.2924 | 162.8403 | 103.8948 | 159.9444 | 156.1593 | 146.5187
30 days | 118.6244 | 102.6724 | 101.3618 | 90.4312 | 91.8806 | 99.3314 | 87.3453 | 84.6583

## Slide 21: RESULTS – Model of Experiment (TOUGHREACT Simulator with Thermodderm Thermodynamic Database) by LBNL
Modeling of experiment shows most elemental concentrations in effluent matching with ICP-MS results
Due to limitations in complete characterization of rock and fluids, some assumptions were made in the model
These assumptions and limitations of model are captured in the next slide

## Slide 22: RESULTS – Model of Experiment
The following uncertainties and limitations are worth noting about modeling of experiment:
Thermodynamic data/models
  Modeled minerals of mixed composition (e.g. clays) may not have the same composition as in the rock formation
  Fluid salinity may exceed the validity range of the implemented ion activity model (extended Debye-Hückel)
Reconstruction of the Produced Fluid compositions
  Anion concentrations computed from assumptions Organic compounds besides acetate were neglected (unknown potential effects on experimental results)
Rock formation mineralogy
  Trace or amorphous minerals (undetected by XRD) impact the system geochemistry – amounts and types were assumed
Sampling effects
  Interactions with atmosphere (O2, CO2 impact pH and redox) Mineral reaction rates (kinetic constants, surface area)

## Slide 23: DISCUSSION
Illitization – Increased illite composition due to breakdown of feldspars which provides the necessary elements for illitization. This phenomenon has been observed in earlier studies such as Guven et al., (1982), where they observed that illitization is favored by high Al concentrations at circum-neutral pH. This is similar to conditions of our experiment
Iron Oxides – The breakdown of pyrite and other iron-bearing minerals release mostly, Fe(II) into solution which is subsequently oxidized to Fe(III) oxyhydroxides that block pores within the formation and lead to permeability losses. The breakdown of pyrite in this study points to high probability of iron oxides formation
Fines Migration – Clay fines migration are occasioned by the deflocculation and dispersal of clay minerals. These subsequently aggregate within flow paths to cause significant permeability losses. High amorphous compositions after reaction observed in this study points to possible clay deflocculation
The cumulative impact of reactions described above is the loss of permeability of formation during long-term post-hydraulic fracturing rock-fluid interactions.

## Slide 24
CONCLUSIONS AND RECOMMENDATIONS
Carbonates, pyrite, feldspars and clays are susceptible to rapid geochemical reactions
Oxidation is a major mechanism in rock-fluid interactions, it leads to breakdown of pyrites
Breakdown of pyrite and other sulfides after exposure to oxygenated fluid leads to generation of acids which cause transient pH reductions, thus catalyzing breakdown of other minerals such as carbonates
Reactions with fluids lead to increased illite content in rock samples suggesting the shift from initially brittle rock to more ductile rock in the long term
Deflocculation of clay minerals leads to the generation of fines which can coalesce later within the fracture to cause blockage of pore-throat (Between 7 to 30 days)
Further work is being done to investigate the cause of illitization observed from XRD measurements
Recommendations:
Longer periods for experiments to help improve model accuracy
Experiment with cored rock samples over longer periods for better replication of rock-fluid reactions in the subsurface
Investigate potential illitization and mechanism that may be responsible

## Slide 25
PLANS AND WORK CURRENTLY IN PROGRESS

## Slide 26
WORKFLOW FOR THE REMAINING EXPERIMENTS
Solid Core Plugs
CT Scanning
XRF
XRD
Indentation Test
Raman Spectroscopy
SEM/EDS
Rebound Hardness
Split Core Plugs
Fracturing Fluid (HFF)
Produced fluid (PF)
Oven
95oC
Fracturing Fluid (HFF)
Produced fluid (PF)
Oven
95oC
7-days
95oC
3-months
95oC
1-month
95oC
6-months
Pre-experiment Data
CT Scanning
XRF
XRD
Indentation Test
Raman Spectroscopy
SEM/EDS
Rebound Hardness
Flow-through
Forward-Flow (3-days with HF)
Reverse-Flow (21-days with PF)
Re-assemble Cored-Rock
Experiment 4
Experiment 5
Experiments designed to complement the initial experiments already undertaken
Experiments include flow-through experiments and extended static batch reactor experiments with cored rock
These experiments are designed to be conducted with core-rock samples
Flow-through experiments will be conducted under dynamic conditions (fluid-flow, temperature, pressure)
Crucial measurements such as pH will be measured at in-situ temperature and pressure conditions
These experiments will provide a closer replication of conditions in the subsurface

## Slide 27
METHODOLOGY
Flow chart of overall project direction and protocols established to achieve objectives
CT Scan and X-ray Fluorescence
Modeling (TOUGHREACT)
Static Batch Experiment
Modeling (TOUGHREACT)
Core Flooding
Experiment
CT Scan and X-ray Fluorescence
Rock-Fluid Interactions
Enable Long-term Prediction
Upscale from Pore to Core
X-ray Diffraction
Electron, X-ray Microscopies
Inductively Coupled Plasma Mass Spectroscopy
Energy Dispersive Spectroscopy
Micro and Nano Indentation
Raman Spectroscopy
Rebound Hardness
Handheld X-ray Fluorescence
X-ray Diffraction
Electron, X-ray Microscopies
Inductively Coupled Plasma Mass Spectroscopy
Energy Dispersive Spectroscopy
Micro and Nano Indentation
Raman Spectroscopy
Rebound Hardness
Handheld X-ray Fluorescence
Rock Powders and Cored Rocks
Cored Rocks (Artificially Fractured)

## Slide 28
CT-Scan – Sample D2H
D2H1
Front View
D2H2
Induced Fracture
Pyrite
Carb
Pyrite
Quartz + clay
Main cutting
Quartz + clay
Side View
Front View
Side View
Solid View
Induced Fracture
Pyrite
Carb
Quartz + clay
Pyrite
Main cutting
Quartz + clay

## Slide 29
CT-Scan – Sample D2V
D2V1
Front View
D2V2
Induced Fracture
Pyrite
Carb
Pyrite
Quartz + clay
Main cutting
Quartz + clay
Side View
Front View
Side View
Solid View
Induced Fracture
Pyrite
Carb
Quartz + clay
Carb
Main cutting
Quartz + clay

## Slide 30
Samples (D2V1)
Combination of CT-Scan, XRF and RBH
Chart: 
| 33.444000000000003 | 33.725999999999999 | 33.720999999999997 | 34.415999999999997 | 34.26 | 34.369 | 34.533999999999999 | 33.945999999999998 | 34.201999999999998 | 34.210999999999999 | 32.140999999999998 | 33.228000000000002 | 32.189 | 33.177999999999997 | 32.335999999999999
Si | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Chart: 
| 2.8330000000000002 | 2.8340000000000001 | 2.5680000000000001 | 4.2990000000000004 | 3.6629999999999998 | 2.9 | 2.968 | 2.544 | 3.4929999999999999 | 3.12 | 3.222 | 3.105 | 2.556 | 2.9079999999999999 | 2.8740000000000001
Fe | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Chart: 
| 1.6839999999999999 | 1.6779999999999999 | 1.716 | 1.603 | 1.635 | 1.6479999999999999 | 1.714 | 1.7230000000000001 | 1.593 | 1.66 | 1.601 | 1.667 | 1.7330000000000001 | 1.647 | 1.665
K | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Chart: 
| 7.3949999999999996 | 7.8250000000000002 | 7.8070000000000004 | 7.532 | 7.9029999999999996 | 7.359 | 7.8109999999999999 | 8.0739999999999998 | 7.3920000000000003 | 7.6429999999999998 | 6.32 | 7.2770000000000001 | 7.343 | 7.0789999999999997 | 6.8079999999999998
Al | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Chart: 
| 0.77400000000000002 | 0.82899999999999996 | 0.64700000000000002 | 0.82199999999999995 | 0.79600000000000004 | 0.85499999999999998 | 0.80800000000000005 | 0.69299999999999995 | 1.101 | 0.82899999999999996 | 0.879 | 0.97799999999999998 | 0.57899999999999996 | 0.871 | 0.72499999999999998
Ca | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Chart: RBH
| 316 | 307.8 | 159 | 131.19999999999999 | 163.6 | 335.8 | 353.8 | 281.2 | 291.39999999999998 | 339.8 | 256.8 | 269 | 247.4 | 236 | 221
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Low Ca throughout
Si, and Al constant on left side and middle
Si drops significantly on the right side
Ca, Si and Fe drops significantly in middle
Fe drops in middle and right side
Generally, ductile and more so in right side
Highest RBH in the middle
Selected Spot for Raman

## Slide 31
CT-Scan – Sample R3H
R3H1
Front View
R3H2
Induced Fracture
Carb
Pyrite
Quartz + clay
Main cutting
Quartz + clay
Side View
Front View
Side View
Solid View
Induced Fracture
Pyrite
Carb
Quartz + clay
Pyrite
Main cutting
Quartz + clay
N. Frac fill

## Slide 32
CT-Scan – Sample R3V
R3V1
Front View
R3V2
Induced Fracture
Pyrite
Pyrite
Quartz + clay
Main cutting
Quartz + clay
Side View
Front View
Side View
Solid View
Induced Fracture
Pyrite
Carb
Quartz + clay
Carb-rich
Main cutting
Quartz + clay
Carb-rich

## Slide 33
Samples (R3V1)
Combination of CT-Scan, XRF and RBH
Chart: RBH
| 163.80000000000001 | 238.6 | 263 | 184.6 | 239.4 | 295.8 | 315.39999999999998 | 236.8 | 255.2 | 228.6 | 261.39999999999998 | 249.2 | 227.6 | 222.6 | 286.8
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Si, Al, and K increase on left side
Si, Al, and K increase in middle portion
Si, Al, and K increase on right side
Fe constant throughout
High carbonate at top and lower portions
Generally, grade from brittle to ductile throughout sample
High RBH in middle
Selected Spot for Raman

## Slide 34
Samples (D2V)
High clay content in ductile samples
Particles of quartz, carbonates and felspars are encapsulated within high amounts of clay matrix
Pyrite occurs as individual pieces and pyrite framboids in other locations

## Slide 35
Samples (R3V1)
Reservoir is characterized by large grains
Relatively Lower clay control on properties as in ductile samples
Particles of quartz, carbonates and felspars are surrounded by clays
Grain-to-grain contacts more prevalent in reservoir

## Slide 36: ACKNOWLEDGEMENTS
I would like to acknowledge that this work was sponsored by DOE Award DE-FE0031776 from the Office of Fossil Energy’s, Oil and Natural Gas Program, U.S. Department of Energy
I am also grateful to my supervisor, Dr. Mileva Radonjic and my PhD. committee members, Dr. James Puckette, Dr. Christine Doughty, Dr. Mohammed Al Dushaishi and Dr. Hunjoo Lee for their immense support and contribution
I am also grateful for the immense support from our research partners at LBNL, Berkeley: Dr. Christine, Dr. Wenming and Dr. Nicolas
Lisa Whitworth and Brent Johnson of Oklahoma State University Microscopy Laboratory for the support during data acquisition
I am appreciative to all current and former group members of Geomimicry and Barrier Materials Group, Vamsi, Allan, Dr. Fengyang, Cody, Havila, Loic and Paschalyn
Our industry partners for providing materials and Caney well production histories.

## Slide 37: REFERENCES
Awejori, G. A., Doughty, C., Xiong, F., Paronish, T., Spycher, N., Radonjic, M. (2022). Integrated Experimental and Modeling Study of Geochemical Reactions of Simple Fracturing Fluids with Caney Shale. Energy & Fuels, 36(17), 10064–10081.
Bratcher, J. C., Kaszuba, J. P., Herz-Thyhsen, R. J., Dewey, J. C. (2021). Ionic Strength and PH Effects on Water–Rock Interaction in an Unconventional Siliceous Reservoir: On the Use of Formation Water in Hydraulic Fracturing. Energy & Fuels, 35(22), 18414–18429.
Chakraborty, N., Karpyn, Z. T., Liu, S., Yoon, H. (2017). Permeability evolution of shale during spontaneous imbibition. Journal of Natural Gas Science and Engineering, 38, 590–596.
Farrokhrouz, M., Taheri, A., Iglauer, S., & Keshavarz, A. (2022). The influence of acidizing on propped fractures for productivity enhancement: Eagle Ford laboratory study. Fuel, 329. https://doi.org/10.1016/j.fuel.2022.125363
Jew, A. D., Druhan, J. L., Ihme, M., Kovscek, A. R., Battiato, I., Kaszuba, J. P., Bargar, J. R., Brown Jr, G. E. (2022). Chemical and Reactive Transport Processes Associated with Hydraulic Fracturing of Unconventional Oil/Gas Shales. Chemical Reviews, 122(9), 9198–9263.
Li, Q., Jew, A. D., Kohli, A., Maher, K., Brown Jr, G. E., Bargar, J. R. (2019). Thicknesses of chemically altered zones in shale matrices resulting from interactions with hydraulic fracturing fluid. Energy & Fuels, 33(8), 6878–6889.
Mukhina, E., Cheremisin, A., Khakimova, L., Garipova, A., Dvoretskaya, E., Zvada, M., Kalacheva, D., Prochukhan, K., Kasyanenko, A., Cheremisin, A. (2021). Enhanced oil recovery method selection for shale oil based on numerical simulations. ACS Omega, 6(37), 23731–23741.
Swami, V., Clarkson, C. R., Settari, A. T. (2012). Non-Darcy flow in shale nanopores: do we have a final answer? SPE Canadian Unconventional Resources Conference.

## Slide 38: THANK YOU
For further enquiries, suggestions and questions, please reach out to us on:
gabriel.awejori@okstate.edu
mileva.radonjic@okstate.edu