## Slide 1: GEOCHEMICAL COMPOSITIONAL CHANGES DUE TO FRACTURING FLUID INTERACTION WITH CANEY SHALE, SOUTH CENTRAL OKLAHOMA, USA
Presenter: Gabriel Adua Awejori
Awejori, G.A., Radonjic, M.
Oklahoma State University, Stillwater, Oklahoma, USA
Spycher, N.
Energy Geosciences Division, Lawrence Berkeley National Laboratory, Berkeley, California, USA
Paronish, T.
Leidos Research Support Team, National Energy Technology Laboratory, Morgantown, West Virginia, USA
DOE Award DE-FE0031776 from the Office of Fossil Energy in Partnership with Continental Resources, OGS, OSU Geology, OSU Chem. Engineering, University of Pittsburgh, Lawrence Berkeley National Lab and DOE NETL.
Goldschmidt Conference 2022, Honolulu, Hawai’i

## Slide 2: PRESENTATION OUTLINE
Introduction
Objectives
Materials & Methods
Results
Conclusions and Recommendations
Figure 1: Caney core on display at workshop in OKC, February 2020. This was recovered from over 650ft interval of drilled well

## Slide 3: INTRODUCTION
The Caney shale is a promising unconventional reservoir located in South-Central Oklahoma Oil Province (SCOOP)
It overlies the Woodford Shale, which is more brittle and has been the target of drilling over the years
Although the Caney shale contains recoverable amounts of hydrocarbons, it has historically been considered a seal or source rock
Relatively less work has been done to fully characterize the geochemical responses of the formation to HFFs for this area

## Slide 4: OBJECTIVES
Investigate Rock-HFF interactions relative to:
Dissolution and precipitation of minerals
Clay swelling and Migration of fines
Petrophysical Impact of Rock-Fluid Interactions

## Slide 5
Characterization of Rock-Fluid Interactions
Modelling (TOUGHREACT)
Batch Experiments
CT Scan and X-Ray Fluorescence
Aid Long-term Prediction
Up-scaling from pore to Core
Experimental and Simulation Design
MATERIALS AND METHODS

## Slide 6: MATERIALS AND METHODS
Fluids Used:
Deionized Water (Base, pH~7)
2% Potassium Chloride Solution (pH~4)
0.5% Choline Chloride Solution (pH~4)
Mineralogical Compositions of Rock Samples
Rock Samples Designation:
HQ – High Quartz
MQ – Medium Quartz, Carbonate and Clay
HC – High Clay

## Slide 7: MATERIALS AND METHODS
Static Batch Experiments
  Static batch experiments at temperature of 95°C and atmospheric pressure
  Designed to mimic shut-in period
  Initial fluid to rock powder ratio of 200mL/g (140mL: 0.7g)
  Sampling undertaken on days 1, 3, 7, 14 and 28 (~10ml each sampling)
  Sampling period approximately 10 minutes
Modelling
  Simple geochemical model of the batch reactor experiment was constructed and modelled using TOUGHREACT, a numerical simulation program
  Assumptions in model included:
    No fluid flow or chemical transport
    Constant temperature and chemical reactions occur with kinetic rates
    Fluid/Rock Powder ratios changed over time due to sampling

## Slide 8: MATERIALS AND METHODS
  X-Ray Diffraction (XRD)
    Mineralogical compositions of samples
  Scanning Electron Microscopy (SEM)
    Dissolution and precipitation patterns
  Inductively Coupled Plasma Mass Spectrometry (ICP-MS)
    Elemental analysis of effluent
  Computed Tomography
  Voxel resolution for scans was 0.43 x 0.43 mm in the XY plane and 0.5 mm along the core axis
  3D volumes are re-sliced along the XZ axis and used as image log
X-ray Fluorescence
  To measure relative elemental abundances along core z-axis
  Mining-Plus suite was run at 6 cm resolution for 60 seconds of exposure time per beam through the entire 650 feet of core

## Slide 9: RESULTS
Chart: Ca-Rich Minerals Dissolution by Rock Type and HFF
| 1 | 3 | 7 | 14 | 21 | 28
HQDI | 7.626 | 11.069 | 11.347 | 14.592 | 15.888 | 18.242
HQKCl | 23.195 | 30.2 | 33.837 | 40.081 | 41.819 | 44.746
HQCCl | 17.039 | 18.997 | 23.818 | 29.726 | 32.638 | 34.524
MQDI | 7.021 | 9.329 | 11.773 | 15.389 | 16.395 | 18.773
MQKCl | 21.685 | 26.4 | 34.619 | 41.477 | 42.225 | 47.893
MQCCl | 16.662 | 18.96 | 24.816 | 32.133 | 34.274 | 37.589
HCDI | 7.519 | 8.932 | 9.736 | 11.628 | 12.254 | 13.524
HCKCl | 21.866 | 25.744 | 32.196 | 37.788 | 37.018 | 39.691
HCCCl | 16.269 | 17.856 | 21.344 | 25.661 | 26.491 | 28.182
KCl
CCl
DI
Red -HQ Blue - MQ Black - HC
HC has least Ca concentration for each fluid
Clay reduces the dissolution of carbonates
Lag in dissolution of carbonates in MQ compared to HQ due to higher clay content in MQ
KCl dissolves carbonates more relative to other fluids for all the rock types
Ability of KCl to stabilize clay allows more fluid to dissolve carbonate minerals
In general, fluid composition is the main driving force for dissolution and precipitation kinetics in rock-fluid interaction for the Caney shale

## Slide 10: RESULTS
Chart: Si-Rich Minerals Dissolution by Rock Type and HFF
| 1 | 3 | 7 | 14 | 21 | 28
HQDI | 11.162 | 17.572 | 28.858 | 42.587 | 53.55 | 58.744
HQKCl | 8.945 | 39.145 | 83.152 | 93.718 | 105.209 | 101.16
HQCCl | 7.645 | 15.315 | 27.753 | 41.419 | 54.326 | 71.082
MQDI | 11.755 | 19.706 | 32.438 | 48.913 | 59.671 | 61.842
MQKCl | 8.612 | 37.381 | 82.952 | 95.782 | 107.321 | 103.428
MQCCl | 7.842 | 15.963 | 29.552 | 49.418 | 72.324 | 90.151
HCDI | 11.049 | 18.635 | 32.503 | 47.219 | 59.831 | 62.753
HCKCl | 9.6 | 43.117 | 86.159 | 97.296 | 108.412 | 106.759
HCCCl | 7.509 | 15.018 | 26.411 | 42.295 | 55.956 | 76.376
KCl
CCl
DI
Red -HQ Blue - MQ Black - HC
Higher Si concentration in effluent
HC and MQ samples having higher Si concentration than HQ
An indication Si in solution is not from dissolution of quartz
Si may be from clay sites or from less stable SiO polymorphs
KCl produces more Si in solution relative to other fluids for all the rock types
Ability of KCl to stabilize clay prevents further elemental exchange between fluid clay sites thus released Si remains in solution

## Slide 11: RESULTS
Chart: Al-Rich Minerals Dissolution by Rock Type and HFF
| 1 | 3 | 7 | 14 | 21 | 28
HQKCl | 0.131 | 0 | 0 | 0 | 0 | 0
HQCCl | 0.52 | 0.353 | 0.178 | 0.194 | 0.111 | 0.1
MQDI | 0.441 | 0.315 | 0.164 | 0.211 | 0.123 | 0.191
MQKCl | 0.121 | 0 | 0 | 0 | 0 | 0
MQCCl | 0.469 | 0.315 | 0.145 | 0.178 | 0.04 | 0.041
HCDI | 0.421 | 0.299 | 0.227 | 0.256 | 0.176 | 0.24
HCKCl | 0.099 | 0 | 0 | 0 | 0 | 0
HCCCl | 0.485 | 0.332 | 0.195 | 0.232 | 0.146 | 0.105
HQDI | 0.456 | 0.392 | 0.258 | 0.243 | 0.146 | 0.206
KCl
CCl
DI
Red -HQ Blue - MQ Black - HC
Al and Mg are the only elements to show sharp drop in elemental concentrations with time
The amount of Al released in solution is very low compared to Si or Ca
The main dynamic causing very low Al concentration in sample is still under investigation
Aluminium decrease could be caused by ion exchange at clay sites of precipitation of Al-based minerals

## Slide 12: RESULTS – Initial Modelling versus Experimental Results
In this experiment, all assumptions were regarded except the period of sampling
When sampling is not considered, only pH values of modelling are in consonance with experimental information
There are significant variations in modelled and experimental information

## Slide 13: RESULTS – Subsequent modelling versus Experimental Results
In this experiment, all assumptions were regarded including the period of sampling
Assumption was that during sampling, extra atmospheric oxygen is introduced into the sample
When sampling is considered, almost all values of modelling are in consonance with experimental information except Sodium
Variations in modelled and experimental information is almost insignificant
Sodium exchange at clay sites during experiments far exceeds what model data provides thus the variation

## Slide 14: RESULTS
Three informal Divisions based on XRF results:
Upper Caney shows decreased Si concentration through heavily bioturbated intervals and Al and Fe rich intervals (Clay and Carbonate Rich Zone)
For the middle Caney, Al and Si concentrations remain consistent whilst Ca is low (Quartz-rich shale zone)
In the lower Caney, sharp increase in Ca is observed whilst Al and Si constant (Carbonate zone followed by High Quartz Shale)

## Slide 15: CONCLUSIONS AND RECOMMENDATIONS
Conclusions:
Carbonates and Clays are more susceptible to geochemical reactions whilst Quartz is relatively unaffected by reactions
High Si concentration in effluent are from Si adsorbed on clay surfaces and from less stable silica polymorphs
Increasing clay composition of samples adversely impact the dissolution of quartz and carbonate minerals
KCl and CCl stabilized clay minerals and promotes dissolution of quartz and carbonates
KCl effected greater stabilization of clay minerals thus leaving initially leached elements in solution, therefore higher concentrations
Greater stabilizing effect of potassium chloride may be explained by the greater ability of potassium cations to exchange for cations in clay interlayers and locking of the interlayers from further interaction with surrounding fluids
Recommendations:
Working on improving geochemical and physical characterization of the rocks and fluid samples for modelling in our next work
Longer periods for experiments to determine the time limits of KCl and CCl effectiveness in preventing adverse clay-fluid reactions especially considering pH values continued increasing throughout the experiment

## Slide 16: ACKNOWLEDGEMENTS
The authors acknowledge:
DOE Award DE-FE0031776 from the Office of Fossil Energy’s, Oil and Natural Gas Program, U.S. Department of Energy
Joseph Renk, Technical Project Officer, National Energy Technology Laboratory
Lisa Whitworth and Brent Johnson of Oklahoma State University Microscopy Laboratory
Brian Killian and Barry Dean of Continental Resources for providing Caney well production histories.
The authors are grateful to Barrier Material and Geomimicry laboratory and Research Group; Dr. Xiong Fengyang, Cody Massion, Allan Katende and Havila Jupudi for their support

## Slide 17: REFERENCES
Dove, P.M. 1995. Kinetic and thermodynamic controls on silica reactivity in weathering environments, in: White, A.F. and Brantley, S.L. (eds). Chemical Weathering Rates of Silicate Minerals. pp. 235–290.
Knauss, K.G., and T.J. Wolery. 1988. The dissolution kinetics of quartz as a function of pH and time at 70 C. Geochim. Cosmochim. Acta 52, 43–53.
Olabode, A.O. 2017. Diagenesis and Formation Stress in Fracture Conductivity of Shaly Rocks; Experimental-Modelling Approach in CO2-Rock Interactions.
Tester, J.W., W.G. Worley, B.A. Robinson, C.O. Grigsby, and J.L. Feerer. 1994. Correlating quartz dissolution kinetics in pure water from 25 to 625C. Geochim. Cosmochim. Acta 58, 2407–2420.

## Slide 18: THANK YOU