## Slide 1
Caney Symposium 2023
M. Radonjic1*, F. Xiong1, A. Katende1, G. Awejori1, C. Massion1
J. Puckette2, Y. Wang2, M. Grammer2,
J. Rutqvist3, Christine Doughty3, S. Nikagawa3,
D. Crandall4, T. Paronish4, J. Renk4
1.Barrier Materials and Geomimicry Lab, Oklahoma State University, Stillwater, OK
2.BPSoG, Oklahoma State University, Stillwater, OK
3.Energy Geosciences Division, Lawrence Berkeley National Laboratory, Berkeley, CA 4.National Energy Technology Laboratory, Morgantown, WV
Corresponding author: mileva.radonjic@okstate.edu
DOE: DE-FE0031776
Field Evaluation of the Caney Shale as an Emerging Unconventional Play, Southern Oklahoma

## Slide 2: Task 6A/12A: Rock-Proppant/Fluid Interactions
Schematics of Tasks 6A and 12A focus:
Fracture conductivity & proppant embedment.
Shale matrix composition, microstructure and gas adsorption.
Long-term effect of geochemical reactivity of Caney shale with Fracturing fluids & its impact on geomechanics & permeability.

## Slide 3: Task 6A/12A: Rock- Fluid/Proppant Interactions: 2D/3DMicrostructural Characterization & Gas Adsorption
The main goal of this subtask is to first identify and quantify microstructural difference between ductile and reservoir/brittle intervals in Caney Shale, including spatial distribution of OM, minerals, porosity, fractures.
The second, we set to do quantitative measurements of matrix components (e.g., OM and inorganic minerals) gas adsorption (CH4/N2), utilizing the data for verification of modeling we applied to predict gas storage potential.
Caney Shale
R1, D1, R2, D2, and R3
Bulk sample
R1, D1, R2, D2, and R3
Powder sample
D2 and R3
SEM/EDS
R1, D1, R2, D2, and R3
LPNA
D2 and R3
HPMA & OK3
D2 and R3
Microstructural and geochemical distribution
Pore structure
Gas storage capacity
Workflow of Comparative Caney Shale
SEMD/EDS: Scanning Electron Microscopy/Energy Dispersive Spectroscopy; LPNA: Low-pressure nitrogen adsorption; HPMA: High-pressure methane adsorption; OK3: three-layer Ono-Kondo model

## Slide 4
The ductile intervals showing fine grained quartz embedded in clay-rich matrix, low nano-porosity and dispersed OM.
The reservoir intervals are overall coarser grained (mainly quartz, carbonates, and feldspars, resulting in a higher heterogeneity and higher micro- porosity.
SEM micrographs and EDS mineral maps (HFW, 508um) showing comparison of spatial composition between ductile& reservoir intervals of Caney Shale samples.
2D Micro-geochemistry of Caney Shale
D2
R3
R2
D1
R1
(a)
(b)
(c)
(d)
(e)
(f)
(g)
(h)
(i)
(j)
(n)
(o)
(s)
(t)
OM
OM
Py
Dol
Qtz
Qtz
OM
Py
OM
Qtz
OM
OM
Dol
OM
OM
OM
Py
Qtz
Qtz

## Slide 5: High-pressure Methane Adsorption
High-pressure methane adsorption isotherms and prediction by Ono-Kondo model of the D2 and R3 Caney Shale samples showing monolayer adsorption in D2 and bilayer adsorption in R3.
Equivalent monolayer for D2
Equivalent multi-layer for R3
Gas adsorption potential, R3 > D2
Results show that the uptake of methane for D2 and R3 (40 MPa and 125 °C) could be ~1.8 and ~4 mg/g (i.e., 2.52 and 5.6 m3/t), respectively.
Schematic of methane adsorption on surfaces of OM & minerals.

## Slide 6: Task6 A/12A: Rock- Fluid/Multiscale Approach to Proppant Embedment and its Impact on Fracture Conductivity
Schematic Illustration of horizontal well completion and proppant placement in fractures, from sand-pack-like packed main vertical fractures to monolayer proppant in secondary fractures.
The main objective is to understand the mechanism(s) and the main parameters & properties that influence proppant embedment in hydraulically fractured Caney shale samples of different lithologies.
A variety of fracture networks are created during hydraulic fracturing, in addition to pre-existing natural fractures.
Proppant placement and distribution is not uniform

## Slide 7
Materials & Methods: Workflow developed for proppant embedment-fracture permeability experimental investigation
Indentation testing at a microscale level to understand proppant shale rock interaction
Understanding the impact of rock lithology and microstructural properties on proppant embedment and fracture conductivity: A case study on the Caney shale, Southern Oklahoma, USA.
American Petroleum Institute(API) fracture permeability testing to investigate fracture conductivity at reservoir conditions using a 6mm proppant pack
Stage 2
Stage 3
Stage 1

## Slide 8: Vertical Fracture: API 19D Fracture Conductivity Testing
Conductivity of the Caney Shale samples, API-19D test
As expected, fracture conductivity decreases with an increase in confining stress, although much lower in ductile samples compared to reservoir samples.
A reduction in confining stress after the maximum confining stress shows that there is no permeability re-instatement even after confining stress is reduced by 50%.
Fracture width change during API-19D test on Caney Shale samples, 50hrs, 2,000 to 12,000, 125oC

## Slide 9
CT scan image of the composite Caney shale sample (five ductile/brittle 1x2 inch plugs) inserted in a carbon composite core holder (12x4 inch).
Fracture conductivity vs overburden pressure
coupling temperatures & pressures.
Fracture conductivity decreases with an increase in confinement stress
Reduced fracture permeability is caused by significantly more severe events, such as proppant embedment and proppant crushing
Flow-Through Monolayer-Filled-Proppant Fracture

## Slide 10: Micro/Nano Mechanical Properties of Caney Shale
Sample D-Ductile 2
Sample E-Reservoir 3
Micro-mechanical properties obtained from indentation
Hardness and elastic modulus vary across the two quadrants even within the same sample.
A lower hardness and elastic modulus implies higher susceptibility to proppant embedment.
Variation in hardness and elastic moduli is due to the heterogeneity of the sample
Allan please change this plot to color one and add some maps to show impact ductile vs brittle indent maps, email back immediately and before 11am

## Slide 11
Task 6A/12A: Rock- Fluid/Caney Shale Geochemical Reactivity
Premise
Declining rates of productivity due to fracture closure significantly influenced by geochemical reactions
Effects of geochemical reactions are pervasive in micro and nano fractures connecting matrix to main fracture network
Objectives
To investigate geochemical changes in the formation during and after hydraulic fracturing – dissolution, precipitation, transformation, swelling, generation of fines
To evaluate the mechanisms controlling geochemical rock-fluid interactions
To evaluate the impact of geochemical changes on permeability of reservoir
Schematic of geochemical rock-fluid interaction within complex fracture system in the subsurface.

## Slide 12: Materials and Methods
Rock
Powder
Fluid
Oven
Well V
V1
V2
V3
Synthetic Fluids
203oF
14.7psi
Well H
H1
H2
H3
Produced
Fluid
7-days
30-days
X-ray Diffraction
Scanning Electron Microscopy
Inductively Coupled Plasma Mass Spectroscopy
Energy Dispersive Spectroscopy
Before
After
Mineralogical Compositions
Chemical Compositions
Effluent Chemistry
Microstructure
Characterization of Alterations caused by Geochemical Reaction
SAMPLE PREPARATION AND STATIC BATCH REACTOR EXPERIMENT
DATA ACQUISITION
DATA ANALYSES AND INTEGRATION
Fracturing
Fluid
Deionized
Water
Modeling

## Slide 13: Mineralogical Alterations of Caney Shale Powders in Field Fracturing Fluids (HF)-XRD
Pyrite breakdown occurs mostly within the first 7 days of reaction
The amount of quartz drops after 7 days but remains relatively constant after that.
Feldspar presence generally shows a downward trend after reaction at both 7 and 30 days
The amount of illite is increasing continuously at 7 and 30 days.
H – Horizontal Well
V – Vertical Well
(7) – 7days reaction
(30) – 30days reaction

## Slide 14: Chemical Composition of Caney-HF Effluent (ICPMS)
Ca concentrations relatively stable because, fracturing fluid used for experiment had a circumneutral pH
Dissolution of pyrite causes transient acidity which initiates dissolution of carbonates
Cation exchange in clay sites also causes Ca concentration in effluent
High concentrations of Si observed on the graphs cannot be explained by quartz dissolution at the given conditions
Dissolution of feldspar contributes to Si concentration in effluent
Dissolution of biogenic silica could explain high Si concentrations
Al is mainly from the dissolution of feldspars
Al entering solution is precipitated at a fast rate – Clays and Al-based minerals
Similar trends observed for Mg and Fe
Chart: Ca Concentration
0 days | 64587.6678 | 64587.6678 | 64587.6678 | 64587.6678 | 64587.6678
7 days | 64553.7075 | 79761.0079 | 76438.0926 | 64662.1624 | 67431.3124
30 days | 74269.4737 | 68096.3221 | 76177.1033 | 77720.5657 | 69471.5693
Chart: Si Concentration
0 days | 6011.3891 | 6011.3891 | 6011.3891 | 6011.3891 | 6011.3891
7 days | 15838.8159 | 15244.6249 | 17204.3504 | 34429.4148 | 18478.708
30 days | 58376.2917 | 30831.6628 | 27068.3162 | 30624.8211 | 46484.4912
Chart: Al Concentration
| V2 | V3 | H1 | H2 | H3
0 days | 272.6525 | 272.6525 | 272.6525 | 272.6525 | 272.6525
7 days | 359.2236 | 415.836 | 326.738 | 307.6723 | 309.5257
30 days | 293.9724 | 265.236 | 300.7823 | 300.9494 | 298.3326

## Slide 15: Mineralogical Alterations of Caney Shale Powders in Field Produced Fluids (PF)-XRD
Pyrite breakdown occurs mostly within the first 7 days of reaction
Composition of quartz drops after 7 days but increase between 7 to 30 days
Feldspar composition reduces and completely absent after 30 days
Illite composition shows an increasing trend over 7 days and decrease marginally between 7 & 30 days
H – Horizontal Well
V – Vertical Well
(7) – 7days reaction
(30) – 30days reaction

## Slide 16
Ca concentrations relatively stable because, produced fluids used for experiment has a circumneutral pH
Dissolution of pyrite causes transient acidity which initiates dissolution of carbonates
Cation exchange in clay sites also causes Ca concentration in effluent
High concentrations of Si observed on the graphs cannot be explained by quartz dissolution at the given conditions
Dissolution of feldspar contributes to Si concentration in effluent
Dissolution of biogenic silica could explain high silica concentrations
Al is mainly from the dissolution of feldspars
Al entering solution is precipitated at a fast rate – Clays and Al-based minerals
Similar trends observed for Magnesium (Mg) and Iron (Fe)
Chemical Composition of Caney-Produced Fluids Effluent
(ICPMS)
Chart: Ca Concentration
| V1 | V2 | V3 | V4 | V5 | H1 | H2 | H3
0 days | 494052.2577 | 494052.2577 | 494052.2577 | 494052.2577 | 494052.2577 | 494052.2577 | 494052.2577 | 494052.2577
7 days | 406614.8321 | 441292.5619 | 403210.5147 | 466723.9245 | 394016.0823 | 421729.7828 | 428776.6468 | 463751.3979
30 days | 431069.7043 | 412014.7063 | 410863.8242 | 439798.5718 | 474640.5789 | 438092.808 | 456574.8855 | 469422.0262
Chart: Si Concentration
| V1 | V2 | V3 | V4 | V5 | H1 | H2 | H3
0 days | 22182.6354 | 22182.6354 | 22182.6354 | 22182.6354 | 22182.6354 | 22182.6354 | 22182.6354 | 22182.6354
7 days | 26156.7483 | 39861.674 | 34208.9818 | 26551.1619 | 22421.1461 | 26178.5648 | 40650.5829 | 24740.6883
30 days | 55978.7873 | 56257.7372 | 61934.8532 | 49012.8589 | 42277.2656 | 49179.5693 | 49306.7985 | 51828.4391
Chart: Al Concentration
| V1 | V2 | V3 | V4 | V5 | H1 | H2 | H3
0 days | 107.7826 | 107.7826 | 107.7826 | 107.7826 | 107.7826 | 107.7826 | 107.7826 | 107.7826
7 days | 170.4136 | 343.7413 | 171.2924 | 162.8403 | 103.8948 | 159.9444 | 156.1593 | 146.5187
30 days | 118.6244 | 102.6724 | 101.3618 | 90.4312 | 91.8806 | 99.3314 | 87.3453 | 84.6583

## Slide 17: Key Observations
Proppant embedment contributes to fracture conductivity reduction especially in fractures with mono-layer proppant
Ductile samples exhibited more damage due to proppant embedment in comparison to reservoir samples.
An increase in confining stress caused a decrease in fracture conductivity due to compaction and crushing of the proppant
Oxygenated fluids cause breakdown of pyrite, increasing acidity in fluid that leads to dissolution of carbonates
High Si concentration in effluent from breakdown of feldspar, biogenic silica and exchange at clay mineral surfaces.
Breakdown of feldspar and/or carbonates resulting in release of ions that can precipitate to cause permeability loss.
Sample preparation impacts XRD. Compared to the ductile intervals, the reservoir intervals are overall coarser grained with a higher heterogeneity and higher micro-porosity.
Caney R3 possesses a higher methane adsorption potential (two times) than Caney D2.

## Slide 18
Caney Symposium 2023
All the data presented is a result of amazing TEAM effort, which includes our staff, students, postdocs, industry collaborators and scientists/faculty from the partnering organizations as well as numerous others who contributed. The following institutions/Groups:
Continental Resources and the the US DOE/NETL, School of Chemical/Petroleum Engineering, CEAT Research Administration, BPSoG, OSU Microscopy Lab, Hamm Institute, Core Labs, Proppant tester, Thermofisher, LBNL, NETL, ORNL, and the individuals who supports us daily:
Brian Kilian and his team, Lisa Whitworth, Brent Johnson, Bipasha Deb, Pam Reynolds, Benjamin Champlin, Kristen &Patrick Wheeler, Dan XX, Denise Stevenson, Tayler Mattie, Ben Anderson, Lisa OConnell, Nic Spycher, Wenming…Kyle Bradford, Rob Krumm, Alex Roubik, Connor Allen, Hannah Whorton and Maria Hernandez,
And some of the former members:
Lashell Williams, Jamie Westmoreland, Carolyn Sanders, Eileen Nelson, Mercy Achang, Guofan Lu, Chris xx, Cody Masion, Havila Jupudi, Andy Rhin, Eric Klyne,
OSU Leadership: Dr. Fahlenkamp and Dr. Knapp, CEAT Deans Tikalsky and Bunting
DOE: DE-FE0031776
ACKNOWLEDGMENTS